## Slide 1: Internship Presentation Summer 2025
Neil Maushard

## Slide 2: Introduction
Mechanical Engineering Student at the University of Illinois
  Minoring in Electrical Engineering
Personal Interests
  Camping and Hiking
  Weightlifting
  Cooking

## Slide 3: Press 19 Die Rack
Problem: Die rack is unorganized and is an ergonomics/safety issue

## Slide 4: Press 19 Die Rack
Measured dies, designed rails to fit them
Determined proper steel tubing and ordered 30 x 2ft
Designed backstop/guide for assembly with proper tolerance

## Slide 5: Press 19 Die Rack
Built prototype using thickest dies for POC and operator approval
Emptied and cleaned rack
Welded tubing

## Slide 6: Press 19 Die Rack
After
Before
Future:
Relabel (?)
Lubricate if needed

## Slide 7: Clad Springback Analysis
Problem: Stainless steel clad’s springback is not well understood
Yellow outline –aluminum bumper
Red outline – clad bumper
Green border – die surface
Green/orange – die
Red – clad bumper scan
Yellow – aluminum bumper scan
Notes: Explain image 1
Explain image 2 and visual springback and measurement process

## Slide 8: Clad Springback Analysis
Chart: Springback Ratio vs Distance from Origin
| 45.096699999999998 | 41.3018 | 37.581600000000002 | 32.343200000000003 | 24.731100000000001 | -45.075699999999998 | -41.2849 | -37.567599999999999 | -32.331499999999998 | -24.721699999999998 | 17.341100000000001 | 11.4215 | -17.340499999999999 | -11.4213 | 0
 | 2.5296 | 2.3395 | 1.838 | 1.3239 | 0.94183 | 2.3619 | 2.1791 | 1.7821 | 1.3435 | 1.0783 | 0.6546 | 0.56058 | 0.78855 | 0.75758 | 0.45153
  Results inconclusive
  Expected a flat line to confirm hypothesis
  Other confounding variables such as previous operations
  Next step is physical experiment
Notes: Explain graph
– axes
What each point is
Expectation, flat or linear
Strong fit
Previous operations

## Slide 9: Clad Springback Analysis
Cut and channeled 3 pieces (clad, steel, aluminum) using same program
Blue – steel
Red – clad
Yellow – aluminum
Discrepancy: steel should be stiffer than aluminum
Measured thickness
  Steel: 0.117 in
  Aluminum: 0.132 in (including PVC)
  Clad: 0.125 in (including PVC)
Try again, ensuring uniform thickness, then rescan
Then bend parts on press 14/15
Notes: Explain initial plan with experiment
Discrepancy
New plan

## Slide 10: Part Marking
Problem: Mecco part marking leads to many inaccuracies
Solution: Mark parts with laser
Started with steel, which goes through post-processing
Tried many different setting combinations
  Power - how much energy is in each laser pulse
  Pulses/mm - how often the laser pulses while traveling
  Pulse width - how long each pulse is
Results were displeasing (?)
  Either look/scan well but too shallow or are deep but don’t scan
Depends on what is required

## Slide 11: Part Marking
Clad doesn’t go through post-processing
Tried a few combinations
Success! But….
  Extra cleaning
Might lead to more clad being run on Bystronic

## Slide 12: Part Marking
Moving Forward
Test aluminum
Integrate marking into Bystronic laser programs
  Bystronic does not have automatic date updates
Explore engraving with Trumpf laser now that we have Bystronic software
  Settings previously determined, but old Trumpf software couldn’t handle barcodes

## Slide 13: Press 217 Manipulator Heads
New set of vacuum and magnet heads for press 217 manipulators

## Slide 14: Press 217 Manipulator Heads
4 purple vacuum heads
4 yellow vacuum heads
4 pneumatic magnet heads
2 manual magnet heads
  2 extra brackets
Saved ~$30,000 by not buying from GCI

## Slide 15: Bystronic Slat Lift
Problem: Bystronic slats degrade over time and need to be rotated out, but are very heavy and hard to move
Solution: Use vacuum lift
Worked with Ramon to design, build, and install a hook onto the vacuum lift
Now slats can be chained to lift
Time to rotate slats reduced from 3 hours to 1 hour

## Slide 16: Raw Bay Reorganization
Problem: Raw bay organization was overcomplicated, and inventory was inaccurate
Solution: simplify
  Shelf specific -> rack specific
  Ex. R1.08.5 becomes R4
Implement audit system to prevent deterioration
Notes: Expected process
Actual process
Why it matters – transporter sub, engineering/maintenance

## Slide 17: Raw Bay Reorganization
Created new labels with larger barcodes and fonts
  Magnetic, allowing for easier changes
Placed new labels and working on taping over old ones with Rafay’s help
Worked with Miguel, Rafay, and Vince to move raw material to new proper place and update inventory
  While updating inventory, we realized inventory was more inaccurate than we thought
Moving forward, raw bay will be audited weekly, ensuring inventory is accurate and material is easy to find
Notes: 3 prong vs 2 prong

## Slide 18: Mast Camera System
Problem: Large masts limit view in large forklifts making higher-up load movements slow and imprecise
Solution: mast camera
Like back up camera, but attaches to front of forklift at fork level

## Slide 19: Mast Camera System - HVS
For one camera system: $2764
Comes with 7” monitor, monitor mount, camera, 6.8Ah battery, battery charger
  Clarks will need 4A model, yellow forklifts will need 3A, big red not compatible
Camera comes with protective mount that bolts on like a fork
Lead time 2-3 weeks

## Slide 20: Mast Camera System - Kocchi’s
For one system: $429 + $97 for spare power bank
Comes with 7” monitor, camera, magnetic power bank
Camera bolts on to fork carriage, we would need to make a simple guard, shown bottom right
Camera connects to power bank, monitor runs on vehicle power
Lead time unknown, company based in China

## Slide 21: Mast Camera System - Cost
Kocchi’s
HVS
 | Qty. | Price | Total
Big Red | 0 |  | $0
Green Clark | 2 | $2,764 | $5,528
Yellow 4-Fork | 1 | $2,764 | $2,764
Total | 3 |  | $8,292
OPTIONAL: |  |  | 
Yellow 2-Fork | 10 | $2,764 | $27,640
New Total |  |  | $35,932
 | Qty. | Price | Total
Big Red | 1 | $526 | $526
Green Clark | 2 | $526 | $1,052
Yellow 4-Fork | 1 | $526 | $526
Total | 4 |  | $2,104
OPTIONAL: |  |  | 
Yellow 2-Fork | 10 | $526 | $5,260
New Total |  |  | $7,364
Kocchi’s will require much more labor
Kocchi’s price includes a spare battery for every system, might not be necessary
HVS does not support Big Red

## Slide 22: Time Studies – Press 117 Blue Bird
Recorded videos of 3-5 press cycles per part
Analyzed videos to find cycle timings accurate to 0.1 seconds
Allows for more accurate quoting and performance expectations
  Also allows for accurate comparisons between press 117 and 217
Trial # | Rear Final Form | CV Blank | CV Preform | T3 Preform | T3 Final Form
Fast Approach (s) | 6.6 | 6.6 | 3.6 | 6.9 | 6.7
Press (s) | 43.9 | 8.8 | 54.8 | 37.8 | 39.8
Retract Slow (s) | 16.4 | 0.0 | 25.1 | 13.9 | 15.6
Cushion Set (s) | 6.2 | 0.0 | 1.2 | 1.2 | 1.7
Rapid Retract (s) | 7.0 | 10.3 | 8.0 | 12.3 | 14.2
Press Cycle (s) | 79.9 | 25.7 | 92.8 | 72.1 | 77.9
Material Handling (s) | 14.8 | 32.9 | 19.3 | 19.0 | 19.1
Total (s) | 94.7 | 58.6 | 112.0 | 91.1 | 97.0
Rate per hour | 38.0 | 61.5 | 32.1 | 39.5 | 37.1
Quoted rate per hour | 40.0 | 48.0 | 40.0 | 40.0 | 40.0
Efficiency vs quote | 95.0% | 128.1% | 80.3% | 98.8% | 92.8%
Notes: Analysis process
Explain material handling

## Slide 23: Conveyor Electrical Cover
Problem: Loose wiring exposed by the electrical cabinet at the conveyor near the Bystronic laser, which is at risk of a forklift jab
Solution: Cover it up
Modeled surrounding area, then designed a cover to protect/hide the wires while keeping them accessible
Next steps: tweak design for ease of assembly
  Get some hinges to attach a top cover
  Add a panel under the cabinet
Notes: Measured surrounding area

## Slide 24: MV2 Sample Support
Assisted in the receiving, cleaning, marking, and repackaging of 30+ new Mack and Volvo samples to be shipped out for inspection

## Slide 25: Takeaways
Hard skills
  Welding
  Creo, AutoCAD
  Machinery Programming
  Working with hands/tools
  Microsoft Office (especially Excel)
Soft skills
  Interdepartmental communication
  Root cause analysis
  Problem solving
  Project priorities
Notes: Future interests – thoughts on manufacturing

## Slide 26: Acknowledgements
ME Team
HR
Everyone!!!